Industrial Laser Cutter
Operation Checklist
1. Add your name, date, time and material to be cut in the operation log.
2. Obtain key from lockbox with authorized code.
3. Turn on water chiller
4. Turn on power to controller (top switch) on right side of machine. The controller will auto-home the laser head.
5. Place work piece inside cabinet and adjust Z axis to ensure it is below the head.
6. Set origin point for job using arrow buttons and press “Origin” button. Press “Reset” to confirm origin is set to correct location, machine will re-home and return to the origin.
7. Set Z-distance from laser carefully using the green Z up/down buttons. This is normally a 7mm gap between the laser head and work piece although depends on the focal length of the lens. Use the step gauge block to set gap distance.
8. Make sure you know the location of the CO2 extinguisher.
9. CLOSE ALL PANELS to avoid laser exposure.
10. Load job onto machine either through PC or USB stick. Job should never specify a laser power of over 50% because it significantly reduces the life of the laser tube. When cutting jobs, it should be for a RUIDA controller G-code.
11. Open the vent blast gate located on exhaust tube above back of machine.
12. Turn on power to exhaust fans (located near the breaker panel).
13. Turn on air assist (pump/compressor).
14. Verify water temperature is between 16 and 25 degrees C. Top off with distilled water if level is low.
15. Turn on laser power supply (middle switch on right side of machine).
16. Select file and press green “Start/Pause” button to start cutting.
17. When job is finished, remove work piece. Controller will beep when job is finished.
18. Close vent blast gate.
19. Turn off exhaust fans if no other vented equipment is in use.
20. Turn off air assist.
21. Turn off laser tube and controller power.
22. Turn off water chiller.
23. Leave the machine clean: empty chip tray and wipe down residue from cut.
24. Finish filling out job log including all required fields and notes on machine performance.
25. Return lock-out key to lock-box.