Spark Studios
Industrial 6090 Laser Cutter Policies
Version: 1.0 : 2026-03-11	Status: Draft

Only authorized persons may use the Industrial “6090” 150W laser cutters (Industrial Laser Cutters) without supervision. Authorized persons may allow others to use the machines, but are responsible for adherence to safety policies and must directly supervise at all times.
Failure to comply with policies may result in revoking privileges to this or other machines.
All authorized persons must re-certify in January of each year with a brief refresher.
Note: This policy refers to the Industrial Laser Cutters with 100W of power or higher and cutting beds of 60cm by 90cm nominal size. The GlowForge laser cutter has a separate policy. Where possible, the GlowForge should be used when the size and power of an industrial laser cutter is not required.
Motivation
The Industrial Laser Cutters can be quite dangerous to the operator, the facilities, and to innocent bystanders. These policies are meant to protect the safety of all. In addition, these systems are complex and expensive to repair or replace. As such, it is important to protect them so that our community can continue to offer this resource.
Process
In order to be granted authorization to use these machines, you must:
- Review this policy document and agree to the provisions.
- Review training materials(TBA) and safety reminders documents and agree to follow them.
- Demonstrate safe operation by running a job under supervision by a certifier. That person must observe and agree that you have followed safe operation. The certifier will evaluate based on evaluation criteria. The certifier may then grant access by revealing the combination to the lock-box containing the lock-out key.
General provisions
- Operators must always monitor the job directly and remain within 10 feet of the machine while it is running a job.
- Operators must not defeat safety mechanisms such as the key lock-out or door close switch.
- Operators must provide their own materials to cut
- Only one user may operate one machine at a time
- Operators must not operate the machines while under the influence of any intoxicant as defined by ORS301.321. Note that this is also part of our code of conduct.
- Machine doors and panels MUST remain closed during operation
- Only approved materials are permitted inside the laser machines (see below)
- No open food or drink is permitted in the lab and near the equipment
- Users must clean up their space and the inside of the laser beds after usage
- Each laser must be operated at no more than 50% of its maximum power rating in order to prevent fires and also extend the life of the laser tube.
- Use of machines MUST be logged.
- In case of fault or emergency-stop, the reason MUST be logged.
- After use, the machine must be locked and the key returned to the lockbox
- The combination to the lockbox must not be shared with unauthorized persons.
- All procedures for unsafe conditions must be followed (see below)
- Vents must be opened and facility ventilation must be active during operation.
- Follow the provided operations checklist when operating the machine.
___Initial

Approved materials
Material	Examples	Notes
Medium-Density Fiber Board	MDF from hardware store	Up to 1/8 inch / Can smell bad, but usually cuts reasonably well with ventilation.
Plywood		Up to 1/8 inch
Acrylic	Plexiglass (make sure it is acrylic)	Cast acrylic gives a better surface-finish
Cardboard	Most ordinary cardboard	Can be a fire hazard, so use with care and be prepared to halt machine and extinguish flare-ups with fire cloth or CO2 extinguisher if needed.
Glass		* For engraving/etching only.
Ceramic tile		* For engraving/etching only.

If you believe a material is safe but is not on this list, please present it along with the Safety Data Sheet (SDS) to the Certifier who can work with the Board to make a decision. If a material is not on the list, it must not be used (even if you think it is safe).
____Initial

Banned materials
Some materials present hazards such as fire (papers), toxic gas (some polymers), or laser exposure (metals). These materials are NOT approved and are likely NEVER to be approved because of the hazards they present.

Material	Examples	Reason
Paper, Cardstock	Printer paper	Fire hazard
Metal	Steel, Brass, Aluminum, chrome, gold, silver	Laser reflection hazard
Mirrored surface	Any type of reflective device	Laser reflection hazard
Polystyrene	Styrofoam	Possible fire hazard
Polycarbonate	Lexan	Toxic gas
ABS	3d printed ABS parts	Toxic gas
Fiberglass		Hazardous glass particles in air and/or toxic fumes from epoxy
Pressure-treated wood	Wood with chemical preservatives	Fire hazard, toxic gas from treatment chemicals
PVC	PVC Pipes, parts, tubes	Toxic (Chlorine) gas
Nylon	Plastic, vinyl, pleather, Sintra, Kydex	Toxic fumes

____Initial

Most laser jobs should be prepared in advance for use on the standard size (55cm by 85cm) laser
cutters. Files to be cut should be SVG (vector) files processed through Lightburn or Gcode files for direct machine instructions.

Unsafe Conditions
It is unlikely, but possible, that during normal operation of the machines, faults may arise that present safety hazards. In these cases, it is extremely important that these procedures are followed to protect operators, nearby persons, the machine, and facilities.

Fire
CO2 lasers are powerful and operate by “burning” material. This can, in some cases, result in an uncontrolled burn of the workpiece or components of the machine. If handled quickly, these flare-ups can be managed, but if allowed to progress can pose a threat to the operator, nearby persons, the machine, and the facility. In case of fire:
- Turn off laser quickly using the Emergency Stop button
- Use the nearby fire blanket CO2 extinguisher to extinguish the flame.
- Remove work piece and revise power and feed-rate to prevent fire in future cuts.
- Log the fire in the operation log.
- If the fire cannot be extinguished, evacuate everyone and call 911 and request fire assistance from emergency services.
___Initial

Laser Lens Vaporization
The laser lenses are made of Selenium. If smoke, debris, or other impurities condense on the focusing lens, the CO2 laser light may vaporize the lens resulting in a reddish-pink residue on the work piece or other surfaces. Because Selenium is a highly toxic material, the following procedures must be followed:
- Turn off laser quickly using the Emergency Stop button.
- DO NOT REMOVE YOUR WORKPIECE, it is toxic and should be considered lost.
- Leave lid closed and ventilation turned on to vent potentially toxic selenium vapor.
- Notify a Spark Studio Board Member
- Turn key to OFF position and leave it locked.
- Place a sign on the machine warning that it is toxic and should not be touched without PPE.
- Log the failure in the operation log
- A board member or other person delegated to clean the residue will don protective equipment (bunny-suit, gloves and respirator) and commence cleaning the area. The machine MUST NOT be operated until it has been cleaned and cleared to operate by the board.
- If you suspect that you have been exposed to Selenium vapor, you are advised to seek medical attention.

___ Initial

Laser Tube Malfunction
The CO2 laser tubes can last a long time, but ultimately they do wear out. In this case, they may physically develop a crack. This may also occur if impurities (such as algae or mold) make their way into the coolant water. If an unusual noise (crackle or pop from the back of the machine) occurs, the laser tube may be failing and you should:
- Turn off laser quickly using the Emergency Stop button.
- Notify a Spark Studio Board Member
- Turn key to OFF position and leave it locked
- Place a sign on the machine warning that it has malfunctioned.
- Log the failure in the operation log
- A board member or other person delegated to maintain the machine will evaluate the failure and work toward remediating it.
___ Initial
Safety Information
The CO2 lasers are inherently hazardous and expensive. Please exercise appropriate caution.

NEVER leave machine unattended while cutting is in progress. If fire occurs, it will spread rapidly and can entirely consume the machine in a matter of minutes.

Follow Operation Checklist in order to keep machine safe, operational, and in a “known” working condition. Report ANY safety or machine damage incident to Spark Studio board members promptly so that safety issues can be mitigated.

NEVER open the hood while the laser is cutting. While there is a safety mechanism to disengage the laser if the hood is open, this should not be relied upon. The infra-red laser beam is not visible to the human eye, but can still cut flesh and cause permanent blindness. Wearing CO2 eye protection (not provided) is also advised to avoid laser exposure. All panels including front hood, back laser tube access and front panel MUST remain closed during operation to avoid direct laser exposure.

In case of fire, laser malfunction, or lens vaporization, E-Stop buttons must be used to turn off the machine. Power off laser and controller and air assist and douse fire with CO2 extinguisher immediately. If fire is not extinguished, call 911 immediately to report the fire and evacuate the building. Report ALL fires to a board member also.

Some materials present safety hazards in the form of toxic gas, fire, and laser light reflection. Do not use any materials not listed on the approved materials list.

The lenses are made of Zinc Selenide and if dirty can vaporize during operation leaving a reddish-pink residue. This substance is acutely toxic. If this occurs, immediately power off machine and leave hood closed with ventilation on. Don personal protective equipment (gloves, respirator, and gown) and scrub down machine to remove residue to avoid possible exposure.

Do not touch lenses or mirrors. Mis-alignment and dirty optics can cause hazards. These are sensitive components and should be handled as little as possible when in normal use. Special alignment procedures are required to clean and re-align optics.
___ Initial

Authorization to use Industrial 6090 150W laser cutter/engraver

I, _____________________________ (person to be authorized) have read and agreed to the Industrial 6090 Laser Cutter Policies. I also understand that doing so may expose me to risks as outlined in the Safety Information. I will accept responsibility for hazards that arise from use and take steps to prevent them.

Signed (person to be authorized) _____________________ Date ____________________

I, ____________________________ (name of Certifier) have agreed that the person named above has demonstrated safe operation and agreed to the policy and safety information.

Evaluation tasks:
- Demonstrated operation through checklist
- Demonstrated fire procedure
- Demonstrated lens vaporization procedure
- Demonstrated tube malfunction procedure

Signed (certifier) _____________________ Date ____________________

Congratulations, you are now authorized to use the laser cutters. The certifier may reveal the combination to the lock-box.